September 28, 2006

Evan Wehr

Ecco Design, Inc.

203 N. 36th Street, #201

Seattle, WA  98103

| Project: | Marzullo Residence Dock |
| --- | --- |
| Location: | 8055 West Mercer Way |
|  | Mercer Island, WA 98040 |
| Permit Application Number: | 0609-038 |

Dear Mr. Wehr:

The City of Mercer Island Development Services has performed a building plan review on the above referenced project for conformance with the following codes, as adopted and amended by the State of Washington and the City of Mercer Island:

2003 International Residential Code (IRC)

2003 International Building Code (IBC), as applicable

2004 Washington State Energy Code, WAC 51-11 (WSEC)

2003 Washington State Ventilation and Indoor Air Quality Code, WAC 51-13 (VIAQ)

2003 Uniform Plumbing Code (UPC)

Mercer Island City Code (MICC)

Please note that you may be contacted by the City Arborist, Fire Marshal, Development Engineer, or Planner with additional comments.

Please respond to the following comments:

Structural

Please detail the connection of the infill area grating to the existing dock framing.

Provide a framing plan and section detail that indicates the location of existing piles and dock framing at areas of the existing dock to be modified or removed.  Verify existing support structure is not compromised by proposed changes.

Provide a plan detail at the connection of the finger pier wood framing to the steel plate at the pile caps and clarify the location and orientation of the boat spikes noted on section A-A.

Provide a framing plan and detail for the framing connection at the juncture of the new finger pier to the existing main pier.

Naturally durable or preservative-treated wood shall be utilized for those portions of wood members that form the structural supports of docks where such members are exposed to the weather without adequate protection from a roof, eave, overhang or other covering to prevent moisture or water accumulation on the surface or at joints between members.  Please note on plans.

Per IBC 2003 Mercer Island Amendment section 3110.4.3 all hardware and fasteners used structurally shall be of a corrosive-resistant metal or be completely protected by a coating of approved paint or corrosive-resistant metal, such as zinc.  Please indicate on plans.

The above comments should be responded to in itemized letter form.  Revisions should be clearly indicated and clouded on the plans.  Resubmit two copies of revised drawings and one copy of structural calculations as required.  If the revisions are minor, you may redmark the plans in person. If you have any questions or require additional clarification, please contact me at (206) 236-7484 or e-mail me at: brian.mcwatters@mercergov.org.

Sincerely,

Brian McWatters

Building Plans Examiner

cc:  evan@eccodesigninc.com