February 22, 2008

Gregory Ashley

16412 NE 10th Place

Bellevue, WA 98008

| Project: | Goldman Rockery Bulkhead |
| --- | --- |
| Location: | 9434 SE 33rd Street |
|  | Mercer Island, WA 98040 |
| Permit Application Number: | 0802-063 |

Dear Mr. Ashley:

The City of Mercer Island Development Services has completed a review of your drawings for conformance with the following codes, as adopted and amended by the State of Washington and the City of Mercer Island:

2006 International Building Code (IBC)

Mercer Island City Code (MICC)

Please note that you may be contacted by the City Arborist, Fire Marshal, Development Engineer, or Planner with additional comments. Please respond to the following comments:

Plan Review Comments:

Please provide dimensional information for the bulkhead, e.g. maximum retained height, depth of rockery keyway excavation, face inclination, minimum width of wall excavation, etc.

Refer to the ARC Rock Wall Construction Guidelines (available at http://www.ceogeo.com/rockwallguidelines.htm) for minimum design guidelines of bulkheads including, but not limited to, the following:

Maximum retained height of six feet.

Minimum keyway depth of two feet.

Reduce hydraulic degrading by extending approved geotextile fabric from toe of rockery to appropriate anchorage at top of excavation.

Please note walls exceeding ARC recommendations or of unusual construction shall be engineered by a Washington State licensed geotechnical engineer.

The above comments should be responded to in itemized letter form. Revisions should be clearly indicated and clouded. Resubmit two copies of revised drawings and one copy of structural calculations as required. If you have any questions or require additional clarification on any of the items contained in this letter, please contact me at (206) 275-7718.

Sincerely,
Paul Skidmore

Senior Building Plans Examiner