May 9, 2008

Mike Cochran

7255 East Mercer Way

Mercer Island, WA  98040

| Project: | Cho Residence |
| --- | --- |
| Location: | 3037 67th Avenue SE |
|  | Mercer Island, WA 98040 |
| Permit Application Number: | 0802-120 |

Dear Mr. Cochran:

The City of Mercer Island Development Services has performed a building plan review on the revisions proposed for the above referenced project for conformance with the following codes, as adopted and amended by the State of Washington and the City of Mercer Island:

2006 International Residential Code (IRC)

2006 International Building Code (IBC), as applicable

2006 Washington State Energy Code, WAC 51-11 (WSEC)

2006 Washington State Ventilation and Indoor Air Quality Code, WAC 51-13 (VIAQ)

2006 Uniform Plumbing Code (UPC)

Mercer Island City Code (MICC)

Note that a response to our last corrections letter dated April 10, 2008 was not provided and several of the items noted in that letter are still unresolved and therefore included below.  Refer to our previous correspondence for additional information.

Please respond to the following comments:

# Structural

- There are numerous holdown locations that appear to require additional framing and hardware directly below to maintain continuity to the foundation, please review and revise plans accordingly at the following locations:

  - Seven of the MST37s at the upper floor grid EEE;

  - Eight of the MST48s along grid AA at the main floor on sheet 4;

  - Two MST48s located at or near the intersection of grids AA and FF on the main floor – this appears to be a cantilever condition without adequate transfer to foundation below;

  - The MST48s along upper floor grid HHH at each side of the window;

  - Eight of the MSTC28s along grid BBB at the upper floor that connect to beams below - verify beam to post and post to foundation connections are adequate at such locations;

  - The holdowns at each end of upper floor grid HHH between the bonus room and bedroom 4 on sheet 6 (see item S3 below).

- The MSTC28s along grid FF at the main floor shear walls appear overstressed for the calculated overturning force, please revise.

- Regarding the 12’ length of upper floor P1-3 shear wall at the bonus room along grid HHH please address the following issues:

  - This wall does not appear to have support framing below – please review and revise floor framing and holdown hardware accordingly;

  - The calculations for the required holdown forces indicate MST48s at this grid line – the MSTC28 holdowns specified on sheet 6 at each end of this wall appear overstressed;

  - Provide detail and/or detail reference to clarify how lateral loads are transferred to the main floor offset shear wall below along grid HH;

  - Provide detail and/or detail reference for the upper wall connection to the roof truss framing – note that the girder truss above appears to be just slightly offset from the wall location and detail 305/S4 may not be appropriate.

- The detail references along grid FFF at the roof framing plan sheet 7 no longer appear to be applicable to this location – please provide correct details and/or detail references for roof framing connections.

- Verify hanger callouts at garage header beams along grid DD as both beams appear to be 8-3/4” wide – an HGLT7 would not be wide enough.

- Clarify connection and provide hardware and nailing specifications for the connections of the new 3-1/2 x 14 PSL along grid DDD to the 8-3/4 x cross-beams below – detail 1/5 does not indicate a positive connection at these locations.

- Detail reference 206/S4 along grid HH and detail reference 201/S4 along grid DD at the upper floor framing plan no longer appear correct – please review and revise.

- Please clarify which plans govern the lateral design and holdown locations to be reviewed by the City Inspector, either the architectural plans (e.g. sheets 1 thru 7) or the structural half-size plans on S2, or both. Verify the information on each is fully and completely coordinated (e.g. there are holdowns indicated on the architectural plans that are not on sheet S2; holdown design may need to be revised per items above).

NOTE: If both plans are applicable then add references to the specific plans on sheet S2 to refer to the appropriate architectural plan for complete lateral design information.

We suggest you contact us to set up a meeting here at City Hall at your earliest convenience to review these outstanding issues in an effort to resolve them in a timely manner.  If you have any questions or require additional clarification, please contact me at (206) 275-7710 or e-mail me at: brian.mcwatters@mercergov.org.

Sincerely,

Brian McWatters

Building Plans Examiner